## Slide 1: EMI from a Slotted Box -Benchmark Simulation Using EMA3D
5/23/2014
Notes: <number>
1/29/2009

## Slide 2: Overview
The electromagnetic interference (EMI) from a slot in a rectangular box has been explored using a FDTD technique and compared to measurements [1]
A FDTD simulation software, EMA3D, has been used to analyze a similar problem and the results are presented herein
The simulation files, results and MATLAB plotting scripts have been provided to assure the validity of the EMA3D modeling results
<number>

## Slide 3: EMA3D Model Setup
Mesh size: Δx = 1 cm, Δy = 0.5 cm, Δz = 1 cm
A thin wire with termination impedances of R1 = 50 Ω, and R2 = 47 Ω was used to model the source line (green line)
A thin gap formalism was used to model the slot (blue line) with a width of 1 mm
Box surfaces (Lx = 22 cm, Ly = 14 cm, Lz = 30 cm) were modeled as perfect electrical conductors (PEC)
A Gaussian pulse voltage source with amplitude 1 mV was used at the R1 end of the thin wire
<number>
R1, Vs
R2

## Slide 4: EMA3D Simulation Setup
A far-field electric field approximation was used to determine the electric field at a 3 m distance from the slot in the benchmark [1]
EMA3D has the ability to obtain far-field approximations similar to the ones performed in the paper
Because the problem is relatively small for the computing resources available, the actual electric field was computed at the 3 m distance
Only the y component of the electric field was considered
<number>
slot
Ey Measurement location
3 m separation

## Slide 5: EMA3D Results Vs. Results in Benchmark [1]
<number>

## Slide 6: Results Comparison
The plots on the previous slide demonstrate that the EMA3D simulation results compare well to the benchmark results [1]
Every cavity-mode and slot generated resonance produced in the benchmark problem is captured in the EMA3D results for delivered power and electric field at 3 m
There are some small differences in some of the peak amplitudes and resonant frequencies
The reason for the small differences could be determined with more time to analyze the problem
However, this analysis was intended to be performed quickly and the result plots demonstrate EMA3D’s ability to accurately produce results using first cut estimates
<number>

## Slide 7: References
M. Li, J. Nuebel, J. L. Drewniak, R. E. DuBroff, T. H. Hubing, T. P. Van Doren, “EMI from Cavity Modes of Shielding Enclosures – FDTD Modeling and Measurements,” IEEE Transactions on Electromagnetic Compatibility, Vol. 42, No. 1, pp. 29 – 38, Feb. 2000
<number>